## Slide 1: Electrical Machines
DC Generator and Motor
Prepared by,
Dr. M. Arun Noyal Doss,
Associate Professor,
EEE, SRM University

## Slide 2: Electrical Machines
Electrical Machine is a device which converts one form of energy into another form

## Slide 3: Classification of Electrical Machines
Electrical Machines
Static
Transformer
Rotating
DC Machines
AC Machines
Generators
Motors
Generators
Motors
Induction
Synchronous
Induction
Synchronous

## Slide 4: Generators
Function:
  Generators are the electrical machines which convert mechanical energy into electrical energy.
Mechanical
Energy
Electrical
Energy
GENERATOR

## Slide 5: Generators
Working Principle
  It works on the principle of Faraday’s laws of electromagnetic induction.
  Whenever a conductor cuts the magnetic field, an emf is induced and current flows when the conductor is connected to a load.
  The direction of induced emf can be found using Fleming’s Right Hand Rule

## Slide 6
FORE FINGER = MAGNETIC FIELD
900
900
900
MIDDLE FINGER = INDUCED
VOLTAGE
Thumb = Conductor
Direction of Induced emf- Fleming’s Right Hand Rule Or Generator Rule

## Slide 7: Illustration of Working Principle of DC Generator using a single turn generator
Conductor
Permanent Magnet – Flux Lines
Prime Mover- to rotate the conductor

## Slide 8: Generators
Working Principle
  Can be explained using velocity components

## Slide 9: Generators-Working Principle
Case I: θ=0o
The velocity component (v) is in parallel with the flux lines or in other words, the angle between the velocity and flux lines is zero.
Hence the emf induced is zero.
E=0

## Slide 10: Generators-Working Principle
Case II: 0o< θ < 90o
The velocity component is making an angle with the flux lines.
The velocity component is resolved into two components
  vsinθ
  Vcosθ
vcosθ is making 0o with respect to flux lines and is not doing any useful work.
The vsinθ is 90o with respect to flux lines and it is doing useful work and due to this, emf is induced.
emin<e<emax

## Slide 11: Generators-Working Principle
Case III: θ = 90o
The velocity component is making an angle 90o with the flux lines.
and due to this, emf is induced.
E=emax

## Slide 12: Generators-Working Principle
For remaining cases, the illustration is shown below,
The emf completes one complete cycle for 360o .

## Slide 13: Emf induced across the Brush
Emf induced is the alternating type
BECAUSE
  during positive half cycle, the conductor comes under the influence of north pole
  during negative half cycle, the conductor comes under the influence of south pole

## Slide 14: How to convert AC to DC?
It is observed that the emf induced is the alternating type, but it is required to obtain unidirectional emf from the DC machines.
The alternating emf can be converted into pulsating dc using the split ring/commutator.

## Slide 15: Commutators
Copper Segments

## Slide 16: Action of Commutators
During positive half cycle, A segment will be at P and B will be at Q.

## Slide 17: Action of Commutators
During negative half cycle, the time at which the current changes the direction, the segment A will move to Q and B will move to P.

## Slide 18: Action of Commutator
The leads to unidirectional current.

## Slide 19: Practical DC Generator
The Major Parts of DC generator are
  Stationary Parts
  Rotating Parts

## Slide 20: Practical DC Generator

## Slide 21: Practical DC Generator
Stationary Parts
  Yoke: Outermost Frame for protection, Mechanical Support to the machine and protects inner parts
  Poles
    Field Windings: This is used to carry field current so it produces the magnetic flux
    Pole Shoe: Horse shoe shape to spread the flux uniformly in the air gap

## Slide 22: Practical DC Generator
Rotating Parts
  Armature
    Slots: cut portion
      Armature Conductors are placed on the slots
    Teeth: uncut Portion
  Commutator: Converts alternating (bidirectional) emf into pulsating dc emf (unidirectional)
  Brush: collect current from the machine and give to a load.

## Slide 23: Stationary Part

## Slide 24: Rotating Part-Armature

## Slide 25: Rotating Part-Armature (Closer View)

## Slide 26: Types of Generator
DC Generators
Separately Excited
Self Excited
Shunt
Series
Compound
Long
Short
Differential
Cumulative
Differential
Cumulative

## Slide 27: Separately Excited
Armature Current
  Ia = IL
Emf Equation
  Eg = V + Ia Ra + Vb
  Vb=brush drop for pair of brush

## Slide 28: Self Excited Shunt
Armature Current
  Ia = IL + Ish
Shunt Field Current
  Ish = V/Rsh
Emf Equation
  Eg = V + Ia Ra + Vb

## Slide 29: Series
Armature Current
  Ia = IL = Ise
  Ia = Ise =IL = V/Rse
Emf Equation
  Eg = V + Ia Ra + Ia Rse + Vb

## Slide 30: Long Shunt
Series Field Current
  Ise = Ia = IL + Ish
Shunt Field Current
  Ish = V/Rsh
Emf Equation
  Eg = V + Ia Ra + Ia Rse + Vb

## Slide 31: Short Shunt
Series Field Current
  Ise = IL
Shunt Field Current
  Ish = (V + Ise Rse)/Rsh
Emf Equation
  Eg = V + Ia Ra + Ise Rse + Vb
Ise

## Slide 32: Characteristics of generators
Open Circuit Characteristics (If, Eg0)
Load Characteristics
  Internal (Ia, Eg)
  External (VL, IL)

## Slide 33
Characteristics of Self excited DC Generator

## Slide 34: Open circuit characteristics-Self excited

## Slide 35: External Characteristics of Self excited dc generator

## Slide 36: Open circuit characteristics of separately excited DC generator
Similar to self
Difference
  voltage build up process is due to both residual magnetism and dc source.

## Slide 37: External Characteristics of Seperately excited
Same as self

## Slide 38: Characteristics of Series generator

## Slide 39: Characteristics of compound generator (long or short)

## Slide 40: Armature Reaction
The interaction of armature flux with field flux is called as armature reaction.
As long as the armature is not connected with the load, there is no armature reaction
When the load is connected to the armature, the current flows in the armature and it produces armature flux. This interacts with the field flux. This is armature reaction.

## Slide 41: Case 1: only field flux, no armature flux
MNA (magnetic neutral axis), GNA (geometric neutral axis) coincides
with each other

## Slide 42: MNA and GNA
MNA: magnetic neutral axis- axis along which there is zero emf. (Commutation axis)
GNA: Geometric neutral axis: axis of symmetry between the poles.

## Slide 43: Case 2: no field, only armature flux
MNA (magnetic neutral axis), GNA (geometric neutral axis) coincides
with each other

## Slide 44: Case 3: Both field and armature flux
Ff
Fd
FA
Fc
Fd-Demagnetising flux opposes Ff
Fc-Cross magnetising perpendicular to Ff
GNA
MNA

## Slide 45: Armature reaction
De-magnetising field reduces the magnitude of field flux so that it reduces the net flux.
Cross magnetizing field distorts the field flux.

## Slide 46: MOTORS
Function:
  Motors are the electrical machines which convert electrical energy into mechanical energy.
Electrical
Energy
Mechanical
Energy
MOTORS

## Slide 47: Motors
Working Principle
  Whenever a current carrying conductor is placed in a magnetic field, the conductor experiences a mechanical force.
  The direction of induced emf can be found using Fleming’s left Hand Rule

## Slide 48
Direction of force- Fleming’s left Hand Rule Or motor Rule

## Slide 49: Illustration of Working Principle of DC Motor
No torque
Case I

## Slide 50: Illustration of Working Principle of DC Motor
No torque
Case II

## Slide 51: Illustration of Working Principle of DC Motor
Case III
Torque, motor rotates in anticlockwise direction

## Slide 52: Types of Motor
DC Motors
Separately Excited
Self Excited
Shunt
Series
Compound
Long
Short
Differential
Cumulative
Differential
Cumulative

## Slide 53: Shunt Motor and back emf
V>Eb
Back emf opposes the applied voltage
N is small, Eb is less, Ia increases
As N increases, Eb increases,
Ia decreases
Eb-acts as self governor

## Slide 54: Back emf
Back EMF – it makes the motor to draw required amount of current from the supply.

## Slide 55: Characteristics of motor
Electrical (Ia, Ta)
Mechanical (Ia,N) and (Ta, N)

## Slide 56: Shunt motor (Ta,Ia)

## Slide 57: Shunt motor – (Ia,N)

## Slide 58: Shunt motor-(Ta,N)

## Slide 59: Series motor

## Slide 60: Series motor
V is constant
Series motor cannot be
Started with no load.

## Slide 61: Series motor

## Slide 62: Compound motors

## Slide 63: Compound motors

## Slide 64: Compound motors

## Slide 65: Applications

## Slide 66: Applications

## Slide 67: Starters
Need
  Starters are used to reduce initial high current

## Slide 68: Why motor draws high current during starting?
At start Back emf is zero, Ia is large

## Slide 83: Induction Machines
Electrical Machine is a device which converts one form of energy into another form

## Slide 84: Classification of Electrical Machines
Electrical Machines
Static
Transformer
Rotating
DC Machines
AC Machines
Generators
Motors
Generators
Motors
Induction
Synchronous
Induction
Synchronous

## Slide 85: Introduction-construction
Stator
  Slots are present
  In the slots, conductors are placed which are connected together to form windings
  Three phase windings are connected in star or delta.
  The stator core is laminated to avoid eddy current loss.
  The material chosen is silicon steel.

## Slide 86: Construction (Stator construction)
The stator is the stationary electrical part of the motor.
The stator core of a National Electrical Manufacturers Association (NEMA) motor is made up of several hundred thin laminations.
Stator laminations are stacked together forming a hollow cylinder. Coils of insulated wire are inserted into slots of the stator core.
Electromagnetism is the principle behind motor operation. Each grouping of coils, together with the steel core it surrounds, form an electromagnet. The stator windings are connected directly to the power source.

## Slide 87: Construction (Rotor construction)
Induction motor rotor types:
  Squirrel cage type:
    Rotor winding is composed of copper bars embedded in the rotor slots and shorted at both end by end rings
    Simple, low cost, robust, low maintenance
  Wound rotor type:
    Rotor winding is wound by wires. The winding terminals can be connected to external circuits through slip rings and brushes.
    Easy to control speed, more expensive.

## Slide 88: Construction (Rotor construction Squirrel cage)

## Slide 91: Squirrel Cage

## Slide 92: Squirrel Cage
/rotor winding
Short circuits all
rotor bars.

## Slide 93: Slip ring rotor

## Slide 94: Slip ring rotor

## Slide 95: Comparison

## Slide 96: Working principle
Current carrying conductor placed in a magnetic field experiences a force.
The two magnetic fields interact with each other to produce mechanical force.

## Slide 97: Working principle
The stator windings are supplied with three phase AC supply.
The rotating magnetic field is produced which rotates with synchronous speed with the constant magnitude of 1.5φm.
The rotating magnetic field sweeps the rotor surface.
The emf is induced in the rotor.
The rotor bars are short circuited and hence current flows in the bars.

## Slide 98: Working principle
The current carrying conductor produces rotor magnetic field which interact with stator magnetic field to produce torque.

## Slide 99: Rotating magnetic field

## Slide 100: Rotating Magnetic Field
The RMF rotates with the magnitude of 1.5ɸm and with the speed of synchronous speed which is given by Ns=120f/p, where f is the frequency and p is the number of poles.

## Slide 101: Synchronous Motor
Constant speed, always run at synchronous speed
Construction similar to alternator.

## Slide 102: Synchronous motor

## Slide 103: Not self Starting motor-Why

## Slide 104: Working Principle
Magnetic Locking Principle

## Slide 105: Magnetically locked and runs

## Slide 106: Procedure to start
Apply Three phase supply
Rotate the rotor using external means and bring the speed of the motor near to the synchronous speed.
Give dc excitation to the field winding of the rotor
At particular instant, the rotor gets locked with the stator and runs with synchronous speed.
Then the external means is disconnected.

## Slide 107: External Means
Ponny Motors-Induction motor
Damper winding
Small DC Motor

## Slide 113
CHARACTERISTICS | SINGLE PHASE INDUCTION MOTOR | THREE PHASE INDUCTION MOTOR
Power Source | Single Phase (1-phase) Only | Generally requires more than a single phase power source (like 3-phase supply).
Starting Mechanism | They are NOT self-starting. | They are self-starting.
Efficiency | Low as only one winding has to carry all the current | High because three winding are available to carry the current
Types | Shaded pole Split Phase Capacitor Start Inductor Run Capacitor Start Capacitor Run | Squirrel cage type Slip ring type or wound induction motor
Cost | Cheaper | Quite Expensive
Slip (s) | There are two slips: Forward slip (s) Backward slip (2-s) | It has only forward slip
Size (for same power rating) | Larger in size | Smaller in size
Power Factor | Low | High
Repair & Maintenance | Easier to repair | Difficult to repair and maintain
Structure | Simple and easy to manufacture | More complicated to construct because of extra components involvement
Starting Torque | Low | High
Operational Reliability | More Reliable | Less Reliable
Motor Rotation | There is no mechanism to change the rotation. | Can be changed easily by changing the phase sequence in stator.

## Slide 114
Applications:
Frequently used for lighter loads. such as: Blowers Vacuum cleaner fans Centrifugal pump Washing machine Grinder Compressor