## Slide 1: 18AIE332T - Image and Video Processing

## Slide 2
Fundamental steps in digital image processing
Components of an image processing system
Structure of human eye, Image formation
Brightness adaptation and discrimination
Basic concepts in sampling and Quantization , Representing digital images
Neighbors of a pixel, Adjacency, Connectivity, Regions and Boundaries
Distance Measures, A simple image formation model
Color fundamentals and models
Fourier transform of sampled functions
Sampling theorem, Aliasing, Obtaining the DFT from the Continuous Transform of a Sampled Function
Properties of 2D DFT
Relationship between spatial and frequency interval, Translation and Rotation, Periodicity, symmetric properties
Fast Fourier Transform FFT
Discrete Cosine Transform DCT
Discrete Wavelet Transform DWT
Some basic intensity transformation functions – image negatives
log transformations
Piecewise linear transformation functions
Digital Image Fundamentals and Image Transforms
SYLLABUS

## Slide 3: Learning Resources
Rafael C Gonzalez, Richard E Woods, “Digital Image Processing”- 3rd Edition, Pearson Education 2008.
2. Yao wang, JoemOstarmann and Ya – quin Zhang, ”Video processing and communication “,1st edition , PH Int.
3. M. Tekalp ,”Digital video Processing”, Prentice Hall International
4. A.K. Jain, “Fundamentals of Digital Image Processing”. Pearson education
5.William K Pratt, “Digital Image Processing”, John Willey (2001).

## Slide 4: INTRODUCTION

## Slide 5: What is a Digital Image?
A digital image is a representation of a two-dimensional image as a finite set of digital values, called picture elements or pixels
Notes: Real world is continuous – an image is simply a digital approximation of this.

## Slide 6: What is a Digital Image? (contd.)
Pixel values typically represent gray levels, colors, heights, opacities etc.
Remember digitization implies that a digital image is an approximation of a real scene
1 pixel

## Slide 7: What is a Digital Image? (contd.)
Common image formats include:
  1 sample per point (B&W or Grayscale)
  3 samples per point (Red, Green, and Blue)
  4 samples per point (Red, Green, Blue, and “Alpha”, a.k.a. Opacity)
For most of this course we will focus on grey-scale images

## Slide 8: What is Digital Image Processing?
Digital image processing focuses on two major tasks
  Improvement of pictorial information for human interpretation
  Processing of image data for storage, transmission and representation for autonomous machine perception
Some argument about where image processing ends and fields such as image analysis and computer vision start

## Slide 9: What is Digital Image Processing? (contd.)
The continuum from image processing to computer vision can be broken up into low-, mid- and high-level processes
Low Level Process
Input: Image Output: Image
Examples: Noise removal, image sharpening
Mid Level Process
Input: Image Output: Attributes
Examples: Object recognition, segmentation
High Level Process
Input: Attributes Output: Understanding
Examples: Scene understanding, autonomous navigation
Notes: Give the analogy of the character recognition system.
Low Level: Cleaning up the image of some text
Mid level: Segmenting the text from the background and recognising individual characters
High level: Understanding what the text says

## Slide 10: History of Digital Image Processing
Early 1920s: One of the first applications of digital imaging was in the news-paper industry
  The Bartlane cable picture transmission service
  Images were transferred by submarine cable between London and New York
  Pictures were coded for cable transfer and reconstructed at the receiving end on a telegraph printer
Early digital image

## Slide 11: History of Digital Image Processing (contd.)
Mid to late 1920s: Improvements to the Bartlane system resulted in higher quality images
  New reproduction processes based on photographic techniques
  Increased number of tones in reproduced images
Improved digital image
Early 15 tone digital image

## Slide 12: History of Digital Image Processing (contd.)
1960s: Improvements in computing technology and the onset of the space race led to a surge of work in digital image processing
  1964: Computers used to improve the quality of images of the moon taken by the Ranger 7 probe
  Such techniques were used in other space missions including the Apollo landings
A picture of the moon taken by the Ranger 7 probe minutes before landing

## Slide 13: History of Digital Image Processing (contd.)
1970s: Digital image processing begins to be used in medical applications
  1979: Sir Godfrey N. Hounsfield & Prof. Allan M. Cormack share the Nobel Prize in medicine for the invention of tomography, the technology behind Computerised Axial Tomography (CAT) scans
Typical head slice
CAT image

## Slide 14: History of Digital Image Processing (contd.)
1980s - Today: The use of digital image processing techniques has exploded and they are now used for all kinds of tasks in all kinds of areas
  Image enhancement/restoration
  Artistic effects
  Medical visualisation
  Industrial inspection
  Law enforcement
  Human computer interfaces

## Slide 15: Applications: Image Enhancement
One of the most common uses of Digital Image Processing techniques: improve quality, remove noise etc

## Slide 16: Applications: The Hubble Telescope
Launched in 1990 the Hubble telescope can take images of very distant objects
However, an incorrect mirror made many of Hubble’s images useless
Image processing techniques were used to fix this

## Slide 17: Applications: Artistic Effects
Artistic effects are used to make images more visually appealing, to add special effects and to make composite images

## Slide 18: Applications: Medicine
X-ray imaging
Gamma-ray imaging

## Slide 19: Applications: Medicine (contd.)
Magnetic Resonance Imaging (MRI)
Ultrasound

## Slide 20: Applications: Medicine (contd.)
3D tomography and rendering with transparencies (1)
3D tomography and rendering with transparencies (2)

## Slide 21: Applications: Medicine (contd.)
Human brain (128 cross-sections)
Cancer cell
(256 cross-sections)
Ice Block (Human brain) (128 cryo-sections)
3D tomography and rendering with transparencies (3)
Take slice from MRI scan of canine heart, and find boundaries between types of tissue Image with gray levels representing tissue density, Use a suitable filter to highlight edges
Original MRI Image of a Dog Heart
Edge Detection Image

## Slide 22: Applications: Geographic Information System (GIS)
Geographic Information Systems
  Satellite imagery
  Terrain classification (LANDSAT)
  Meteorology (NOAA)

## Slide 23: Applications: Geographic Information System (GIS) (Contd.)
Night-Time Lights of the World data set (infra red)
  Global inventory of human settlement
  Not hard to imagine the kind of analysis that might be done using this data

## Slide 24: Applications: Industrial Inspection
Human operators are expensive, slow and unreliable
Make machines do the job instead
Industrial vision systems are used in all kinds of industries
Can we trust them?

## Slide 25: Applications: PCB Inspection
Printed Circuit Board (PCB) inspection
  Machine inspection is used to determine that all components are present and that all solder joints are acceptable
  Both conventional imaging and x-ray imaging are used

## Slide 26: Applications: Law Enforcement
Image processing techniques are used extensively by law enforcers
  Number plate recognition for speed cameras/automated toll systems
  Fingerprint recognition
  Enhancement of CCTV images

## Slide 27: Applications: Human–computer interaction (HCI)
Try to make human computer interfaces more natural
  Face recognition
  Gesture recognition
Does anyone remember the user interface from “Minority Report”?
These tasks can be extremely difficult

## Slide 28: Fundamental Steps in Digital Image Processing

## Slide 29: Fundamental Steps in Digital Image Processing

## Slide 30: Fundamental Steps in Digital Image Processing (Contd.) Image Aquisition
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Image Acquisition: The first step is to acquire a digital image using a digital camera, scanner, or any other image capture device.
The image can be obtained from various sources such as photographs, videos, or medical imaging devices.

## Slide 31: Fundamental Steps in Digital Image Processing (Contd.) Image Enhancement
Image Enhancement: Image enhancement techniques aim to improve the visual quality of the image or highlight specific features of interest.
Common enhancement techniques include filtering operations like sharpening, blurring, and noise reduction.
Other methods like contrast stretching, histogram modification, and spatial domain operations can also be applied.
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression

## Slide 32: Fundamental Steps in Digital Image Processing (Contd.) Image Restoration
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Image restoration is used to recover images that have been degraded by noise, motion blur, or other distortions.
It involves techniques such as image deblurring, denoising, and image inpainting to reconstruct the original image as accurately as possible.

## Slide 33: Fundamental Steps in Digital Image Processing (Contd.) Morphological Processing
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Morphological processing is a fundamental technique in digital image processing that deals with the shape and structure of objects within an image.
It is based on mathematical morphology, which analyzes the geometrical properties of objects by using set theory and algebraic operations.
Morphological processing is particularly useful in tasks such as image segmentation, noise removal, object detection, and image analysis.

## Slide 34: Fundamental Steps in Digital Image Processing (Contd.) Segmentation
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Image segmentation involves partitioning an image into meaningful regions or objects.
It helps in object recognition, image understanding, and computer vision tasks.
Techniques like thresholding, region growing, edge detection, and clustering algorithms are used for segmentation.

## Slide 35: Fundamental Steps in Digital Image Processing (Contd.) Object Recognition
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Object recognition is a computer vision task that involves identifying and classifying objects or specific patterns within digital images or video frames.
The goal is to enable machines to understand and interpret visual data, similar to how humans perceive and recognize objects in their surroundings.
Object recognition has numerous practical applications, including autonomous vehicles, surveillance systems, augmented reality, robotics, and image retrieval.

## Slide 36: Fundamental Steps in Digital Image Processing (Contd.) Representation & Description
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Representation and description are crucial steps in the process of analyzing and interpreting digital images.
These steps involve transforming the raw pixel data into meaningful and informative representations that capture the essential characteristics of objects or regions of interest within an image

## Slide 37: Fundamental Steps in Digital Image Processing (Contd.) Image Compression
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Image compression reduces the storage space required for images while minimizing the loss of visual quality.
Compression techniques such as JPEG (Joint Photographic Experts Group) and PNG (Portable Network Graphics) are widely used to achieve efficient storage and transmission of images.

## Slide 38: Fundamental Steps in Digital Image Processing (Contd.) Colour Image Processing
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Color image processing involves the analysis, manipulation, and enhancement of images that contain color information.
It deals with images represented in color spaces such as RGB (Red, Green, Blue), CMYK (Cyan, Magenta, Yellow, Black), HSV (Hue, Saturation, Value), or other color models.
Color image processing techniques are used in various applications, including computer vision, medical imaging, remote sensing, and digital photography.

## Slide 39: Components of an Image Processing System

## Slide 40: Components of an Image Processing System Image Sensors
Starting with image sensing, there are two elements required to acquire digital images.
The first is a physical device that is sensitive to the energy radiated by the object we wish to image.
The second, called a digitizer, is a device for converting the output of the physical sensing device into digital form.
For instance, in a digital video camera, the sensors produce an electrical output proportional to light intensity.
The digitizer converts these outputs to digital data

## Slide 41: Components of an Image Processing System (Contd.) Specialized Image Processing hardware
Specialized image processing hardware usually consists of the digitizer just mentioned, plus hardware that performs other primitive operations, such as an arithmetic logic unit (ALU), that performs arithmetic and logical operations in parallel on entire images.
One example of how an ALU is used is in averaging images as quickly as they are digitized, for the purpose of noise reduction.
This type of hardware sometimes is called a front-end subsystem, and its most distinguishing characteristic is speed.
In other words, this unit performs functions that require fast data throughputs (e.g., digitizing and averaging video images at 30 frames/s) that the typical main computer cannot handle.

## Slide 42: Components of an Image Processing System (Contd.) Computer
The computer in an image processing system is a general-purpose computer and can range from a PC to a supercomputer.
In dedicated applications, sometimes custom computers are used to achieve a required level of performance, but our interest here is on general-purpose image processing systems.
In these systems, almost any well-equipped PC-type machine is suitable for off-line image processing tasks.

## Slide 43: Components of an Image Processing System (Contd.) Image Processing Software
Software for image processing consists of specialized modules that perform specific tasks.
A well-designed package also includes the capability for the user to write code that, as a minimum, utilizes the specialized modules.
More sophisticated software packages allow the integration of those modules and general-purpose software commands from at least one computer language.

## Slide 44: Components of an Image Processing System (Contd.) Mass Storage
Mass storage capability is a must in image processing applications. An image of size pixels, in which the intensity of each pixel is an 8-bit quantity, requires one megabyte of storage space if the image is not compressed.
Digital storage for image processing applications falls into three principal categories:
short-term storage for use during processing, (Frame Buffer)
(2) on-line storage for relatively fast recall
(3) archival storage, characterized by infrequent access.

## Slide 45: Components of an Image Processing System (Contd.) Image Displays
Image displays in use today are mainly color (preferably flat screen) TV monitors.
Monitors are driven by the outputs of image and graphics display cards that are an integral part of the computer system.
Seldom are there requirements for image display applications that cannot be met by display cards available commercially as part of the computer system.
In some cases, it is necessary to have stereo displays, and these are implemented in the form of headgear containing two small displays embedded in goggles worn by the user.

## Slide 46: Components of an Image Processing System (Contd.) Hardcopy
Hardcopy devices for recording images include laser printers, film cameras, heat-sensitive devices, inkjet units, and digital units, such as optical and CDROM disks.
Film provides the highest possible resolution, but paper is the obvious medium of choice for written material.
For presentations, images are displayed on film transparencies or in a digital medium if image projection equipment is used.
The latter approach is gaining acceptance as the standard for image presentations.

## Slide 47: Components of an Image Processing System (Contd.) Networking
Networking is almost a default function in any computer system in use today.
Because of the large amount of data inherent in image processing applications, the key consideration in image transmission is bandwidth.
In dedicated networks, this typically is not a problem, but communications with remote sites via the Internet are not always as efficient.
Fortunately, this situation is improving quickly as a result of optical fiber and other broadband technologies.

## Slide 48: Self Test Questions
1. Which step involves extracting relevant information or features from an image?
a) Image Enhancement
b) Image Restoration
c) Image Segmentation
d) Feature Extraction
Answer: d) Feature Extraction
2. What is the process of assigning labels or class identities to objects in an image called?
a) Image Recognition
b) Image Analysis
c) Image Compression
d) Image Segmentation
Answer: a) Image Recognition
3. Which step involves presenting processed images or analysis results in a visually meaningful form?
a) Image Visualization
b) Image Analysis
c) Image Restoration
d) Image Enhancement
Answer: a) Image Visualization
4. What is the final step in digital image processing?
a) Image Acquisition
b) Image Enhancement
c) Image Analysis
d) Image Visualization
Answer: d) Image Visualization

## Slide 49: Self Test Questions
5. Which component of an image processing system captures images from various sources?
a) Image Analysis Algorithms
b) Preprocessing Components
c) Image Acquisition Devices
d) User Interface
Answer: c) Image Acquisition Devices
6. Which step involves converting an image from one color space to another?
a) Image Acquisition
b) Image Compression
c) Color Image Processing
d) Image Analysis
Answer: c) Color Image Processing
7. Which step involves partitioning an image into meaningful regions or objects?
a) Image Acquisition
b) Image Segmentation
c) Image Restoration
d) Image Analysis
Answer: b) Image Segmentation
8. What is the process of recovering images that have been degraded by noise or distortions called?
a) Image Compression
b) Image Segmentation
c) Image Restoration
d) Image Recognition
Answer: c) Image Restoration

## Slide 50: Self Test Questions
9. What is the first step in digital image processing?
a) Image Enhancement
b) Image Acquisition
c) Image Compression
d) Image Analysis
Answer: b) Image Acquisition
10. Which step in digital image processing involves reducing noise and enhancing image quality?
a) Image Segmentation
b) Image Enhancement
c) Image Compression
d) Image Recognition
Answer: b) Image Enhancement
11. What are the names of the various color image processing categories?
a) Pseudo-color and Multi-color processing
b) Half-color and pseudo-color processing
c) Full-color and pseudo-color processing
d) Half-color and full-color processing
Answer: c) Full-color and pseudo-color processing
12. Which of the following process helps in Image enhancement?
a) Digital Image Processing
b) Analog Image Processing
c) Both a and b
d) None of the above
Answer: c) Both a and b

## Slide 51: Thank You