## Slide 1
“EMERGENCY PREPAREDNESS”
Unit-2

## Slide 2: Why Emergency Preparedness
To take prompt corrective actions to save lives and sufferings/injuries.
To protect plant machines, equipments & buildings etc.
To protect loss of materials.
To Protect and minimize property losses.
To resume normal situation or operation within
minimum
possible time.

## Slide 3: NEED OF EMERGENCY PLAN
AFTER BHOPAL GAS DISASTER IN 1984, THE FACTORIES ACT 1948 WAS AMENDED IN 1987 AND NEW PROVISIONS REGARDING SAFETY AND
MANAGEMENT
WERE
EMERGENCY ADDED.
NOW IT
IS A MANDATORY TO AN
ORGANISATION TO PREPARE EMERGENCY PREPAREDNESS PLAN HANDLING HAZARDOUS CHEMICALS AS PER MSIHC RULES 1989.
UNDER THE PROVISION OF SECTION 41B (4) OF FACTORIES ACT 1987, EVERY OCCUPIER SHALL HAVE VALID EMERGENCY PLAN FOR HIS FACTORY.

## Slide 4: SCOPE
EMERGENCY PLAN COMES IN TO EFFECT AT THE DECLARATION OF
TO TERMINATION OF
EMERGENCY AND EXTENDS UP
THE
EMERGENCY.
IT IS APPLICABLE
EMPLOYEES AND
AVAILABLE IN
TO ALL PERSONS
THE
PLANT/FACILITY.

## Slide 5: Emergencies
On site emergency is caused by an accident that takes place in a chemical installation and effects are confined to the industry premises involving only people working in the industry
.
If an accident takes place in a chemical industry/unit and its effects are felt outside its premises, the situation thus called off site emergency

## Slide 6: Onsite emergency plan
Appointment of key persons
Site controller
Incident Controller
Administartive Manager
Fire and Safety Officer
Dept. Heads
Infrastructure
Emergency control centre
Assembly points
Declaration of off site
Rehearsals – on-site

## Slide 7: Objectives of the Emergency Plan This plan is a standing instructions for handling 'Emergency Situations.
The plan envisages pooling of resources to
mitigate emergency.
To safe guard human beings, machines, equipments and property.
To safeguard other persons not affected by emergency so far.
Identify/rescue the casualties and arrange for their treatment.
To define channels of communications with key personnel.

## Slide 8: Contents of Emergency Plan
The emergency plan for industrial facilities
should include:
Brief Process description
Various hazards available
Classification of emergencies
Emergency scenario envisaged
Agencies required for Emergency handling
Declaration and notification of emergency
Emergency Control centre and assembly areas
Communication facilities available
First-aid centre and hospital facilities

## Slide 9: Continue…
Responsibilities of key personnel/Alternate persons with contact numbers.
Monitoring of hazardous chemicals.
Fire fighting and rescue arrangements.
Assessment of conditions subsequent to release of toxic chemicals, rescue.
Termination of emergency and notification of the same.
Maintenance of emergency equipments.
Surveillance and record keeping.
Mutual aid scheme members and communication system among members.
Periodicity of conducting drills/exercises.

## Slide 10: Identification of hazards
Process Hazards
Hazards, Temperature
Chemical Hazards, Pressure
Hazards,
Cryogenic hazards
Natural calamity
Flood, Earthquake, Psunami
Electrical Hazard,
Missile Attack, terrorist attack, sabotage etc.

## Slide 11: ACCIDENT SCENARIOS
Massive leakage of toxic chemicals from
process piping / equipment.
failure of vessel, piping of
Catastrophic chemical.
Major fire
Leakage of a road tanker containing hazardous chemicals likely to affect our site.
Severe lightning / storm condition /
flooding of plant area due to excessive rain.
Severe earth quake and / or any explosion near the plant
Air craft or missile impact on / near the
Plant.

## Slide 12: Means for declaring emergency
Emergency Siren : It is operated from main Control Room. Power supply to the siren is class III, (backed by diesel generator).
Public Address System: Public address system is provided at main Control room and it covers entire plant area and buildings. Power supply to P.A. system is class III (backed by diesel generator).

## Slide 13: Declaration of emergency
signals 5
for a
Commence :- Short intermittent seconds 'ON' & 5 Seconds 'OFF' total period of 2 minutes.
Termination :- A continuous signal (All clear) for 2 minutes.
Emergency announcement
Emergency announcement on PA System shall be made in English, Hindi & Gujarati language.

## Slide 14: RESOURCES
Public
Communication systems (including
Address System)
Emergency Siren
Transport for evacuation of plant personnel
Assembly area
First Aid facility including ambulance at site
Fire Fighting and rescue arrangements
Security arrangements
Breathing air sets and facilities for bottling of breathing air.
Laboratory facilities
Monitors of Cl2, POCl3 , n-butanol & Explosi
meter
Fire Alarm System –Heat & Smoke Detectors
Fire Pump House

## Slide 15: Site Emergency Director
Emergency Director and is
Occupier /factory manager shall be Site
overall
Controlling Authority.
On hearing the emergency siren or on getting information of the same he shall proceed to the emergency control center and take over as Site Emergency Director.
He will assess the emergency situation based upon the information and data provided.
He will direct
handling of the emergency
situation.
He will arrange to intimate / liaise with
authorities in DAE / AERB / HWB, Mumbai
He will arrange to send causalities for treatment.

## Slide 16: Advisory Group
Advisory Group will assemble in emergency control centre and advise Site Emergency Director
in consultation with Shift-In-
control
Charge and damage group.

## Slide 17: Damage Control Group
Damage Control Group members shall assemble immediately in main control room on hearing siren.
Provide necessary assistance to SI to co- ordinate the jobs pertaining to their sections for combating the emergency and controlling the damage.
Carry out head count in their respective sections and report missing persons to Site Emergency Director.
Follow up the progress of the handling of the emergency.
Give feed back to SI / Site Emergency Director for terminating the emergency as soon as the situation eases
Assess the losses and report to General Manager.

## Slide 18: Station Officer
On getting information he will immediately reach the fire station/ scene of fire and take charge of fire fighting / rescue operations etc. depending upon the situation.
Till Dy CFO / Station Officer arrives on the scene the sub-officer / LFM on duty will take charge of the activities.
He will ensure that necessary information is passed on to OIECR / GSFC / IPCL (Reliance Industries Limited) / GR / VMC fire services for immediate help through hot line or any alternate means of communication, if assistance is required in his opinion.

## Slide 19: Information Officer
listed under 'Channels of
He will inform the officers Communication-Intimation of
Emergency' about
declaration of emergency.
Information Officer is the only authorized channel through whom information should be given out into public domain. The Information Officer shall periodically collect all information, status of the emergency and maintain a chronological record of the events. He will be responsible for the receipt and transmission of information on the emergency and the control measures in progress to the appropriate authorities as per direction & advice by the SED.
He will arrange for augmenting transport, ambulance, security and other facilities as required.
Depending upon the situation he will assist SED to inform the relevant state Govt. Authorities i.e. Collector, Police
recognized
as per the
Commissioner, General Hospital & other hospital and ask for necessary assistance instructions of SED.

## Slide 20: Security Officer / Asst. Security Officer:
On hearing / getting information about the emergency, he shall restrict entry of the personnel to the plant site as per the directions given by the SI / SED.
He shall regulate the personnel movement into the plant site and no outsiders other than fire services shall be permitted through main gate.
GSFC fire services shall also be permitted through north gate, which should be opened immediately on declaration of emergency.
He shall not hold fire tenders from IPCL, GSFC, VMC fire services, Gujarat Refinery at gate during emergency at site.
He shall inform the listed fire brigades on instructions from Dy CFO
/ SI / SED.
He shall inform to hospitals etc. on instructions from SED/ Adm. Officer / Security Officer / Medical officer.
The ASO will also inform the local officers under 'Channels of Communication-Intimation of Emergency' about declaration of emergency.

## Slide 21: Emergency Management
Natural or man-made causes, which is beyond the coping capacity of the affected community.
Disaster Management involves a continuous and integrated process of planning, organising, coordinating and implementing measures.
Measures are necessary for:
Prevention of danger or threat.
Mitigation of risk , severity or consequences.
Prompt response during emergency.
Assessing the severity or magnitude.
Evacuation, rescue and treatment.

## Slide 22
Continue……
Therefore such situations and risks should be visualized, assessed and planned to tackle successfully within the shortest time.
Hence there is a need for consideration of safety aspects right through the design, siting, construction and operation stages.
All the aspects anticipated from manmade and natural disasters are to be considered during the design of the plant.
Emergency management Plan should be
of
made available for handling any type emergency.

## Slide 23: General information
Seismic Zones
Average wind speed
Wind direction
Rain fall Earth quake
Max. and Min. Temp
Air port
Railway Station
School /College
Highway etc
SITE AREA MAPS

## Slide 24: Emergency action plan,
Maintenance of emergency preparedness,
Records,
Periodicity of conducting drills/exercises,
Public awareness programmes and
Training of plant personnel and public
authorities.
The Regulatory Body shall formulate guidelines on counter measures to be
taken at various intervention levels, along with derived intervention levels in the case of off-site emergencies. Action plans, based on these guidelines and other requirements in the off-site emergency plans, for nuclear and radiation facilities in general, are described in detail in the Safety Guidelines for preparation of emergency

## Slide 25
Mutual Aid Scheme
There is a mutual aid scheme in off Site Industrial Emergency Control Room situated in materials building of Reliance Industries of which HWP, Baroda is a member.
This is headed by Collector and District Magistrate, Vadodara and is manned round the clock.
A wireless base station located in Fire Station of HWP, Baroda connects to Off-site industrial emergency control room (OIECR).
Hot line telephone facility from HWP,

## Slide 26: Emergency Control Center
An emergency control center is established for use during the emergency. Its location is in the General Manager's office, in technical building (housing all necessary communication gadgets including STD telephones, wireless, GSFC telephone, HWP telephone and communication lists and formats and other appliances as listed). The Meeting room in main control room will serve as the alternate Emergency Control Center. Direction of emergency activities should be transferred from the plant control room to emergency control center/alternate Emergency Control Center as soon as possible to enable plant operators to perform system and field operations without disturbance.

## Slide 27: Assembly Point & Escape routes
Multipurpose hall near security gate is declared as assembly point during emergency in the plant. All persons will assemble in the multipurpose hall if they are asked to do so.
All person will remain present at their work place, in case of site emergency is in local zone only and not effecting health of plant employees.
In case of evacuation is forced from the plant due to emergent situation, an announcement will be made through PA system to all employees to assemble in the assembly hall. All persons (except emergency staff) will assemble section wise in multipurpose hall. The senior most person of each section will make head count and report to Site Emergency Director. The plant persons may be shifted to safe place by available means, if requires.
All plant persons will walk through different roads / emergency exits marked in the plant to assemble in multipurpose hall in case of emergency.
All persons will follow escape route and will reach multipurpose hall (Assembly point) after hearing announcement made though PA system.

## Slide 28: LIST OF EQUIPMENT IN EMERGENCY CONTROL ROOM
B.A. Sets / Escape packs 2 Nos.
and Plant Layout
SEPP with Baroda Area Map, drawing
Plant system flow sheets
Safety Report
Pre-calculated concentrations of toxic release at various distances
Photographs from plant and surroundings
Black / white board
Adequate copies of Formats as given in SEPP
Up to date Communication lists and contact numbers
Rubber / PVC & Canvas hand gloves
Safety Helmets to Individuals
Communication gadgets, P&T phone, fax, GSFC phone, internal phone.

## Slide 29: LIST OF EQUIPTMENT IN AMBULANCE
Stretchers
Bed, Pillows
First Aid Box
Oxygen Cylinder

## Slide 30: LIST OF EQUIPMENT IN FIRST AID CENTRE
Bed - One No.
Treatment Cabin
Water Tap & Sink
Oxygen Apparatus - 2
Stretchers
Bandage of various types
Antibiotic
Various required medicines.

## Slide 31: SAMPLE FORMATS
FORMAT FOR
DECLARATION OF SITE EMERGENCY
EXERCISE
Attention all plant personnel.
Site Emergency exercise is being conducted at HWP, Baroda.
There is ……………………. describe briefly the incident, its location, affected areas and any other relevant information…………………………………………………………………
……….…………………………………………………………………………
……………………………………………………………………………………
……………………………………………………………………………………
…………………………..
Please note this is only an exercise.
( to be repeated in Hindi and Gujarati )

## Slide 32: FORMAT FOR TERMINATION OF SITE EMERGENCY EXERCISE
Attention all plant personnel.
The Site Emergency exercise has been terminated.
( to be repeated in Hindi and Gujarati )
……………………………………………………………………
…………………………
Site Emergency is declared at HWP, Baroda.
Please note, this is emergency exercise only.
( to be repeated in Hindi and Gujarati)

## Slide 34: Reference documents
MSIHC Rules, 1989 amended in 2000.
AERB Safety Guideline no. AERB
/ SG / EP-3 titled “preparation of site emergency preparedness plans for non-nuclear installations" issued in August, 2000