## Slide 1
CHEMICAL PLANT SAFETY
UNIT-2
c

## Slide 2
Hazard
A hazard is generally anything that can hurt you or make you ill.

## Slide 4: Hazardous chemical
A material that has physical or chemical characteristic of potential for causing harm
human injury,
damage to property,
damage to environment
or some combination of these is known as hazardous chemical.

## Slide 6
Hazardous chemicals

## Slide 7
Hazardous chemicals

## Slide 9: Chemical Hazard
The undesired effects which are caused with the absorption of hazardous chemicals by the human body- are called chemical hazards.
The hazardous chemicals
concentration, or when mixed
alone in with other
chemical substance, can cause injury, disease or death.

## Slide 10: Hazard label – NFPA (National fire protection Association) Diamond

## Slide 11: TYPES OF CHEMICAL HAZARD
HEALTH HAZARD- Health hazards are chemical, physical or biological factors in our environment that can have negative impacts on our short- or long-term health
PHYSICAL HAZARD- Physical hazard are based on the intrinsic properties of the chemical.

## Slide 12: PHYSICAL HAZARD
Flammable gases
Flammable aerosols
Oxidizing gases
Gases under pressure
Flammable liquids
Flammable solids
Self-reactive substances and mixtures
Pyrophoric liquids
contact with water, emit flammable gases
Oxidizing liquids
Oxidizing solids
Organic peroxides
Corrosive to metals
Combustible dusts
Pyrophoric gases

## Slide 13: HEALTH HAZARD
Acute toxicity
Skin
corrosion/irritation
Serious eye damage/eye irritation
Respiratory or skin sensitization
Germ cell mutagenicity
Carcinogenicity
Reproductive toxicity
Specific target organ toxicity – single exposure
Specific target organ toxicity – repeated exposure
Aspiration hazard
Bio hazardous infectious materials

## Slide 15: Types Of Chemical Hazard
Naturally Occurring Chemicals
Ex. Mycrotoxin, Pyrrolizidine Alkaloides Intentionally Added Chemicals
Ex. Preservatives: Nitrite and Sulfiting agents. Unintentionally Or Incidentally Added Chemicals Ex. Pesticides, Lead, Arsenic, Mercury.

## Slide 16: WHMIS
Workplace Hazardous Materials Information System Goals-
Prevent Health Hazards
Reduce Accidents

## Slide 17
CLASSIFICATION OF DANGEROUS GOODS/CHEMICALS –under motor vehicle rules 1989
CLASS 1- EXPLOSIVES
An explosive substance is a solid or liquid substance which itself capable of producing chemical reactions and gas at such a temperature, pressure and speed to cause damage to surroundings
Causes:
Mass explosion hazard
Projection hazard
Fire hazard and either minor blast hazard or minor projection hazard
Give rise to radiant heat
Burn one after another producing minor blast

## Slide 18
CLASS 2 – GASES: COMPRESSED, LIQUIFIED OR DISSOLVED UNDER PRESSURE
2.1 Flammable gases – Chemical which mixes in air in its gaseous state at normal pressure and becomes flammable. Its BP at normal pressure is below 20 °C
2.2 Non Flammable, Non toxic gases - gases which are transported at a pressure not less than 286 kPa at 20 °C or as refrigerated liquid and which are asphyxiant or oxidizing
2.3 Toxic Gases – toxic or corrosive to humans as they pose a hazard to health (LC50 value =< 5000ppm

## Slide 19
CLASS 3 – FLAMMABLE LIQUIDS
These are liquids or a mixtures of liquids / liquids containing solids in solution or suspension which has a flash point <61 °C
CLASS 4
4.1 Flammable solids (easy ignition by external sources such as sparks, flames)
4.2 Spontaneously combustible (spontaneous heating under normal conditions, heating up in contact with air)
4.3 Dangerous when wet (liq/sol interact with water – flammable spontaneous)
CLASS 5
5.1 Oxidizing substances (directly/indirectly evolve oxygen
5.2 Organic peroxides – liable to exothermic decomposition at normal/elevated temp

## Slide 20
CLASS 6:
6.1 Toxic substances – liable either to cause death/serious injury /harm human health
6.2 Infectious substances – containing viable microorganisms, including bacterium, virus, parasite, fungus causes diseases to human & animals
CLASS 7:
Radioactive materials – spontaneously emit radiation
CLASS 8:
Corrosives – severely damaging living tissues
CLASS 9:
Miscellaneous Dangerous substances and articles
Substances not falling with other classes /divisions
Lachrymatory substances not falling with other classes

## Slide 21
Hazardous Material Description

## Slide 23: Effect of chemicals depends on several factors
The routes of entry
The physical properties of the substances
Work practices
The nature of the exposure
Combined exposures
The susceptibility of workers
Toxicity

## Slide 24: Effect Of Chemicals
Causing irritation
Allergies
Lack of oxygen
Systemic poisoning
Cancer
Damage to the unborn fetus
Effects on the future generations
Pneumoconiosis (Dusty lung)

## Slide 35
Handling of chemicals

## Slide 40
Chlorine storage tanks
Ammonia storage tanks
Double walled Ammonia storage tank
Details of storage
Year of installation
Capacity in tons
Material of construction
Relevant standard
Type pf protective painting
Designed pressure and temperature
Working pressure and temperature
Safety device against over pressure
Safety device against temperature, liquid level
Details of venting system
Storage Inspection
General information:
Name and location of storage
Name and address of the occupier
Availability of safety data sheet

## Slide 43: Controlling Chemical Hazards in the Workplace
•
Reduce or eliminate the use of hazardous chemicals whenever possible.
•
Maintain adequate ventilation systems to reduce concentrations of airborne chemicals.
•
Practicing good personal hygiene (e.g. washing hands) and maintaining regular workplace cleaning routines.
•
Learn how to avoid carrying hazardous substances home.

## Slide 44
Introduce administrative controls to minimize exposure to chemicals (e.g. rotate workers through different jobs or locations.
Perform maintenance work in off-hours so that accidental release of toxic substances will affect fewer workers).
Use personal protective equipment and devices.
Maintain equipment in good order to prevent leaks and breakdowns that may release toxic substances.

## Slide 53: General Tips for Chemical Safety
Read the warning labels on any chemical before you use it.
Remember that an unlabeled chemical is a dangerous one. ever sniff or smell an unlabeled chemical.
Followthe directions and precautions listed on the label and ways dispose of a chemical properly.

## Slide 60: TOXICOLOGY

## Slide 61: “All substance are poisons”; there is none, which is not a poison. The dose differentiates a poison and a remedy.

## Slide 62: Sources of Toxin:
Environment
Food/Feed/Water
Drugs

## Slide 63: Environment
Air Pollution
Carbone monoxide
Nitrogen oxides
Smoke
Poor Ventilation
Ammonia, Hydrogen Sulfide
Volatile Compounds
Chlorine, Hydrocarbon fuels

## Slide 64: Toxicity
Toxicity is the degree to which a substance can damage an organism.
Toxicity can refer to the effect on a whole organism, such as an animal, bacterium, or plant as well as the effect on a substructure of the organism, such as a cell (cytotoxicity)or an organ such as the liver (hepatotoxicity).
Toxicity is the capacity of a chemical compound to produce injury.

## Slide 65: Some possible outcomes of Toxicant:
Death after a short period of time- Acute toxicity
Cancer / mutation in DNA
Skin / eye irritation
Fertility problems
Carcinogenicity / mutagenicity
Reproduction effects
Sudden heart failure and death

## Slide 68: Types of Toxicity
Acute toxicity
Sub-acute toxicity
Sub-chronic toxicity
Chronic toxicity

## Slide 69: Conditions of strong poisoning
High temperature
Deep or rapid breathing
Long working hours
Combination of two or more poisonous substance

## Slide 70
Median Lethal Concentration (LC50)-
LC50:
Concentration of a toxicant
(mg/m3) in air to kill 50% of the
animals exposed
for the specific
length of time.
LD50 is the amount of a material, given all at once, which causes the death of 50% (one half) of a group of test animals. The LD50 is one way to measure the short-term poisoning potential (acute toxicity) of a material
LD50:
In toxicology, the median lethal dose, LD₅₀, LC₅₀ is a measure of the lethal dose of a toxin, radiation, or pathogen.
Lethal Dosage 50

## Slide 71
Threshold Limit Value (TLV)
TLVs are generally defined as air concentrations of chemicals that most workers can be exposed to for an 8-h workday, 40h per week for a working lifetime without suffering adverse effects.
Short-term exposure limit (STEL) is a 15-min time-weighted average exposure that should not be exceeded during the workday even if the 8-h TWA is within the TLV.
•Exposures at the STEL should not be repeated more than four times per day
Zone A – irritation
Zone B – coughing
Zone C – breathing difficulty
Zone D – collapse
Zone E – death